Fixing skew on a milling machine
Contrary to what is said in the PR, in this document the “machine” coordinate system is defined by the mechanical setup, and the “bed” coordinate system is an unskewed coordinate system.
We set our coordinate system such that -
1. The Z axis is perpendicular to the bed
2. The machine Z axis unit vector is in the XZ plane
3. The origin is coincident with the machine origin (i.e. we do not concern ourselves with the offset required to correct for the position of the endstops).
Therefore, the machine unit vectors are -
vec {X_m} = langle u_x, 0, u_z rangle	vec {Y_m} = langle v_x, v_y, v_z rangle	vec {Z_m} = langle w_x, w_y, w_z rangle
If the Z axis were not perpendicular to the bed, then the spindle would plunge into the work at an angle. We can either accept this, or we can have a situation where the bed moves while the spindle is plunging so as to keep the motion of the spindle vertical. The latter is worse than the former, which is why we set the machine Z axis perpendicular to the bed. Therefore vec {Z_m} = langle 0, 0, 1 rangle , and machine coordinate of (x, y, z)_machine is at langle x u_x + y v_x, y v_y, x u_z + y v_z + z rangle_bed
We get the machine to go to the 4 corners of a parallelogram a = ( 0, 0 )_machine ; b = ( x_0, 0 )_machine c = ( 0 , y_0 )_machine ; d = ( x_0, y_0 )_machine and lower the Z axis until it touches and marks the bed. We measure the machine Z coordinates of the bed, and we get -
widevec {a} = (0, 0, 0)_machine = langle 0, 0, 0 rangle_bed	widevec b = ( x_0, 0, z_0 )_machine = langle x_0 u_x, 0, 0 rangle_bed widevec c = ( 0, y_0, z_1 )_machine = langle y_0 v_x, y_0 v_y, 0 rangle_bed	widevec d = ( x_0, y_0, z_2 )_machine = langle x_0 u_x + y_0 v_x, y_0 v_y, 0 rangle_bed
If the Z axis is not actually perpendicular to the bed, these marks won’t be in the place we need them to be. However, since the axis should be nearly perpendicular and/or the distances z_0, z_1 "and" z_2 should be small, the error should be very small. We use the marks to measure the distance on the bed surface from the origin to b, c and d. The square of those distances are -
ldline ab rdline ^2 = x^2_0 u^2_x ldline ac rdline ^2 = y^2_0 ( v^2_x + v^2_y ) ldline ad rdline ^2 = x^2_0 u^2_x + y^2_0 ( v^2_x + v^2_y ) + 2 x_0 u_x y_0 v_x = ldline ab rdline^2 + ldline ac rdline^2 + 2 x_0 u_x y_0 v_x
We also have ldline bc rdline ^2 = x_0^2 u_x^2 + y_0^2 ( v_x^2 + v_y^2 ) - 2 x_0 u_x y_0 v_x = ldline ab rdline ^2 + ldline ac rdline ^2 - 2 x_0 u_x y_0 v_x
We then derive -
u_x = { ldline ab rdline } over { x_0 }, v_x = { ldline ad rdline ^2 - ldline bc rdline ^2 } over { 4 x_0 y_0 u_x }, v_y = sqrt { { ldline ad rdline ^2 - ldline ab rdline ^2 - y_0 v_x ( y_0 v_x + 2 x_0 u_x ) } over { y_0^2 } }
We note
x_0 u_z + z_0 = 0 ; y_0 v_z + z_1 = 0
from which we derive
u_z = - { z_0 over x_0 } ; v_z = - { z_1 over y_0 }

## Worked example

widevec X = langle 0.97, 0, 0.008 rangle ; widevec Y = langle 0.006, 0.981, 0.002 rangle ; widevec Z = langle 0, 0, 1 rangle
	MACHINE				BED
	X	Y	Z		X	Y	Z
a	0	0	0		0	0	0
b	20	0	-0.16		19.4	0	0
c	0	15	-0.03		0.09	14.715	0
d	20	15	-0.19		19.49	14.715	0

Line	Length	Squared
ab	19.4	376.36
ac	14.715...	216.539325
ad	24.421...	596.391325
bc	24.277...	589.407325

u_x = 19.4 over 20 = 0.97 ; v_x = { 596.391 - 589.407 } over { 4 times 15 times 20 times 0.97 } = 0.006

v_y = sqrt { { 596.391325 - 376.36 - 0.006 times 15 times ( 0.006 times 15 + 2 times 20 times 0.97 ) } over { 15^2 } } = 0.981

u_z = - { -0.16 over 20 } = 0.008 ; v_z = - { -0.03 over 15 } = 0.002